## Slide 1
The smart way
of thinking
— within HVAC/R and indoor air quality

## Slide 2
Mission Statement
“We provide non-metal HVAC/R solutions for air distribution and air dispersion that create outstanding value for our customers, beyond what any traditional or conventional ventilation solution has ever done.
For more than 40 years we’ve refined our technology with two simple ideas in mind: make it better and make it easier.
Our systems are easy to order and easy to install, which
is why our customers consider us reliable and easy to do
business with. We never compromise on quality and always aspire to be superior when it comes to design and service.”

## Slide 3
Who is FabricAir?
OUR HISTORY
1973
IPS Ventilation (part of Electrolux)
launches the world’s first Fabric Air
Dispersion System
1995
FabricAir is ISO 9001 certified
1997
FabricAir USA is established
2002
FabricAir UK is established
2003
FabricAir Lithuania is established and
production is moved to Alytus
2007
FabricAir Germany is established

## Slide 4
OUR HISTORY
2012
FabricAir Norway is established
2017
FabricAir Spain is established
2008
FabricAir Turkey is established
2016
FabricAir China is established
Who is FabricAir?

## Slide 5
AIR DISPERSION & AIR DISTRIBUTION
FabricAir Products

## Slide 6
FabricAir Products
UNDERFLOOR DUCTING

## Slide 7
FabricAir Products
INSULATED DUCTS

## Slide 8
FabricAir Products
LAYFLAT DUCTS

## Slide 9
CUSTOM DUCT PROFILES
FabricAir Products

## Slide 10
DROP DIFFUSERS
FabricAir Products

## Slide 11
DESIGN
FREEDOM
If you can do it in conventional ducting you can do it in fabric ducting.
Elbows
Reductions and transitions
Outlet branch
Location of outlet flow models are flexible
Cones are most often not needed
Why Fabric Duct?
DESIGN FREEDOM
Notes: …some features are similar to conventional ducting
Elbows – made with the exact angle desired. There are no restrictions as to direction or dimensions.
Reductions and transitions (all transitions and reductions are made in fabric). Based on the suspension system chosen, the optimum transitions and reductions are selected.
Outlet branch – transition from a main duct to a side duct through an outlet branch.
Location of outlet flow models are flexible around the circumference.
Cones are optional. Cones are most often not needed.

## Slide 12
The design of fabric systems varies from job to job
– the possibilities are endless.
DESIGN FREEDOM
Why Fabric Duct?
DESIGN FREEDOM
Notes: System design is flexible
Because fabric ducts are not composed of fixed bends, elbows and lengths, the product offers complete freedom in design.
…more
The fabric systems are dimensioned and constructed based on online 3D drawing and configuration tools.

## Slide 13
Fabric Ducts Can Be Designed With Different Shapes
DESIGN FREEDOM
Why Fabric Duct?
DESIGN FREEDOM
Notes: System design is flexible
…in most cases the versatility is greater.
…more
The design of fabric systems varies from job to job – the possibilities are endless. It is easy to create fabric systems fitting the layout of the building perfectly. Naturally, the systems are supplied with both elbows, main and side ducts, reductions etc. Since a fabric system does not require balancing, the need for dampers is minimized and the design work is simplified – while the indoor climate is optimized.

## Slide 14
All fully integrated in a FabricAir System
No extra noise reduction is needed
No extra grills or diffusers are necessary
No damper is necessary
No inconvenient shortenings or assembly on site
No extra insulation is necessary
Painting is not necessary
COST
ADVANTAGE
COST ADVANTAGE
Why Fabric Duct?
COST ADVANTAGE
Notes: Skip conventional thinking
Many functions known from conventional metal ducts are fully integrated in a fabric system. Diffusers, grilles, dampers etc. are completely redundant. A fabric system is all inclusive.
No extra grills or diffusers are necessary. The fabric system functions both as a duct system and as an air dispersion system.
No damper is necessary. A fabric system does not require balancing.
Painting is not necessary. The fabrics are dyed.
No extra insulation is necessary. A fabric system is condensation free.
No inconvenient shortenings or assembly on site. A fabric system fits straight from the factory, is assembled with zippers and is ready for suspension as soon as it arrives.
No extra noise reduction is needed (except perhaps reduction of fan noise). Noiseless is the standard.

## Slide 15
AIR DISPERSION
HOMOGENITY
Dead Zones Are Eliminated by using an Air Dispersion System, the entire system is a diffuser.
The air is evenly distributed throughout the length of the fabric system.
Conventional ducts distribute air at certain points i.e. via diffusers.
Why Fabric Duct?
AIR DISPERSION HOMOGENITY

## Slide 16
Why Fabric Duct?
SILENT
WORKING
Reduced noise level
Maximum level for TV Studios; 25 dB(A)
Why Fabric Duct?
SILENCE

## Slide 17
In Fabric Ducts;
Flow speeds are very low and adjustable
FLOW
SPEED
No
Draft
Why Fabric Duct?
FLOW SPEED

## Slide 18
HYGIENE
Hygiene level is Far Better Than Conventional Metal Ducts
◼ Antibacterial
◼ No Condensation
◼ No Need For Insulation
◼ Washable
Why Fabric Duct?
HYGIENE

## Slide 19
◼ The installation time is 4-5 times quicker than conventional metal systemss
◼ On average our customers save 100 hours per project due to the ease of installation
◼ On average that means we have saved contractors more than 77,000 work days last year
◼ On a typical installation, a contractor can save a minimum of 70% on installation time
®
FabricAir Fabric Ducts
Why Fabric Ducting?
COST SAVINGS

## Slide 20
◼ We invented facric ducting in 1973
◼ We apply high-tech laser cutting technology, which cuts 1,000 holes per second
◼ We tailor 1 million meters of ducting a year and process 1.2 million m2 fabric a year
◼ We deliver on time with 99.4% punctuality and with an impressive lead time of <13 days from order release to arrival on job site
®
FabricAir Fabric Ducts
Why Fabric Air?
COMPANY FACTS

## Slide 21
◼ Fabric ducting is an energy friendly alternative to conventional metal solutions
◼ The lower pressure loss saves up to 30% on your energy bill
◼ Expected lifespan of a fabric solution is more than 30 years, in fact some of the original 1970’s ducts are still in use
◼ The compact nature of the fabric ensures 21.3 times less CO2 emissions from transportation than an equivalent solution in metal
®
FabricAir Fabric Ducts
Why Fabric Ducting?
ENERGY

## Slide 22
SUSPENSION
TYPES
Products
FABRICS
FabricAir® Trevira is a permeable fabric and comes in 3 variants.
It is suitable in places where there is a risk of bacteria growth or condensation, such as the food industry or indoor pools.

## Slide 23
SUSPENSION
TYPES
Products
FABRICS
FabricAir® Combi is available in 8 variants with both permeable and non-permeable fabric.
The fabric is strong and durable – fabric variants come with a 5 or 10 year warranty.

## Slide 24
SUSPENSION
TYPES
Products
FABRICS
FabricAir® Lite is available as
non-permeable fabric in 4 variants.
The fabric is strong and durable –
anti-microbial and anti-static features
are optional.

## Slide 25
SUSPENSION
TYPES
Products
FABRICS
FabricAir® Glass 220 is
non-combustable and non-permeable.

## Slide 26
SUSPENSION
TYPES
Products
FABRICS
FabricAir® Poly is a non-permeable fabric, mainly used in heavy industrial installations for distributing isothermal or heated air.

## Slide 27
FLOW
MODELS
Products
FLOW MODELS
Different Flow Models for different Applications

## Slide 28
SUSPENSION
TYPES
SUSPENSION TYPES
Products
FLOW MODELS
In FabFlow™ the air exits the duct through the permeable fabric surface.
The air is driven by thermodynamic forces preventing drafts in the occupied zone, which results in a high level of comfort.

## Slide 29
SUSPENSION
TYPES
SUSPENSION TYPES
Products
FLOW MODELS
With MicroFlowTM the air exits the duct via laser cut micro-perforations along the circumference of the duct.
The micro-perforations can cover between 90° and 360° of the duct’s circumference. MicroFlowTM has the smallest near-zone of all of the perforated fabrics available.
In most cases the near-zone will not extend beyond 300 mm [11.81”].

## Slide 30
SUSPENSION
TYPES
SUSPENSION TYPES
Products
FLOW MODELS
With PerfoFlowTM the air exits the duct via laser cut perforations along the circumference of the duct.
The perforations can cover between 90° and 360° of the duct’s circumference.
The size of the near zone depends on the static pressure inside the duct, the percentage of the circumference that is perforated, and the size and spacing of the perforations.

## Slide 31
SUSPENSION
TYPES
SUSPENSION TYPES
Products
FLOW MODELS
SonicFlowTM is a directional flow model where the air exits the duct via rows of laser cut perforations.
Multiple rows of SonicFlowTM can be specified for a duct, with each row covering a maximum of 30° of the circumference.
The throw depends on the static pressure inside the duct, the size, and spacing of the perforations.

## Slide 32
SUSPENSION
TYPES
SUSPENSION TYPES
Products
FLOW MODELS
OriFlowTM is a directional flow model where the air exits the duct via rows of laser cut orifices.
Multiple rows of OriFlowTM can be specified for a duct.
The throw depends on the static pressure inside the duct, the size, and spacing of the orifices.

## Slide 33
SUSPENSION
TYPES
SUSPENSION TYPES
Products
FLOW MODELS
NozzFlowTM is used in applications where very precise directional airflow is needed.
The discharge coefficient is almost at unity due to the shape of the nozzle.
This results in higher discharge velocities than an equivalently sized orifice, and longer more directional throws.

## Slide 34
SUSPENSION
TYPES
SUSPENSION TYPES
Products
FLOW MODELS
JetFlowTM is capable of generating exceptionally long throws through the use of conical jets in varying diameters.
The jets have a very high discharge coefficient due to the conical shape.
This results in higher discharge velocities than an equivalently sized orifice.

## Slide 35
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 1 / Type 1 AIO
Simple on straight runs
Inexpensive
Available in galvanized and stainless steel
Available with All-in-One

## Slide 36
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 2
Great for larger diameters
Simple on straight runs
Inexpensive
Available in galvanized and stainless steel

## Slide 37
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 3 / Type 3 AIO
Quick and easy installation for regular ceilings
Easy removal for frequently washed applications
Inexpensive
Available with All-in-One

## Slide 38
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 4
Great for larger diameters
Easy removal for frequently washed applications
Inexpensive

## Slide 39
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 5 / Type 5 AIO
Aesthetically pleasing installation
Stable installation
Available with All-in-One

## Slide 40
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 6
Aesthetically pleasing installation
Stable installation
Great for larger diameters

## Slide 41
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 7
Aesthetically pleasing installation
Stable installation

## Slide 42
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 8 / Type 8 AIO
Our most versatile system
Excellent for vertical and complicated systems
No seismic requirements in most areas
Available with All-in-One

## Slide 43
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 11 / Type 11A
Great for low ceiling heights
Aesthetically pleasing installation

## Slide 44
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 12
Great for low ceiling heights
Great for frequently washed applications
Inexpensive

## Slide 45
SUSPENSION
TYPES
Products
SUSPENSION TYPES
Type 13
Aesthetically pleasing installation
Flexible in high ceiling heights
Great for larger diameters
Stable installation
Great for frequent wash applications

## Slide 46
SUSPENSION
TYPES
Applications
◼ FOOD
◼ SPORT
◼ INDUSTRIAL
◼ RETAIL & PUBLIC AREAS
◼ EDUCATIONAL, OFFICES & COMFORT
◼ MEDICAL INDUSTRY

## Slide 64
LOOK UP FOR A CHANGE